## Slide 1: EEE 304 Digital Electronics Laboratory Project Update Presentation FSM Based Ticket Vending Machine (TVM) using FPGA
Group NO. 04
ID:
2006009
2006011
2006018
2006025
Section: A1

## Slide 2
Outline
Objectives
Introduction
Methodology
State Diagram
Sample Output

## Slide 3
Objective
Design a Digital FSM Architecture for a Ticket Vending Machine (TVM)
Implement Ticket Selection Logic
Incorporate Rebate Logic
Generate Output Signals for Ticket Dispensing

## Slide 4
Introduction
What is a Ticket Vending Machine?
A Ticket Vending Machine (TVM) is an automated device that issues tickets, typically for public transportation, such as buses, trains, or trams.
This project proposes a FSM based digital logic scheme for a Ticket Vending Machine where passengers can buy tickets with simple operation.

## Slide 5
Key components of a TVM
Source and Destination Station Selection
Ticket Number Selection
Rebate System (Discounts)
Payment Option
User Interface
Printing
We will only focus on the digital logic part on this project.

## Slide 6
Key Features of the Proposed TVM
Ticket Selection
Mothijheel
For Our Project we will design the TVM operating for Five Metro Stations.
Each passenger can get at most two tickets at a time.
According to the selection of station and total number of stations total cost will be calculated.

## Slide 7
Key Features of the Proposed TVM
Rebate System
Students, physically challenged and senior citizens will get a discount of 5 Tk on the cost of each ticket, by providing a code assigned to them.
After they enter the code, the software matches the code with database and if the code matches, that passenger will get a discount

## Slide 8
Key Features of the Proposed TVM
Money and Change:
There will be four types of money (5/10/20/50 tk)
If the inserted amount is equal to the cost, then the ticket will be dispensed.
And if the amount is larger, the change is returned with the ticket.
If the amount is smaller, process will continue till input money is greater or equal than cost.

## Slide 9
Methodology

## Slide 10
Methodology

## Slide 12
Methodology
Taking Input
In our CPLD Board we have 8 Input pins. Each Input Pin will be assigned to necessary input variables.
We have four pulse switches which is also assigned necessary Variables.
Also, global clock for 7 Segment Display will be given from inbuild clock from the CPLD board.

## Slide 13
8 Input Pins
(Leveled As SW1 to SW8)
4 Pulse Switches
(PS1 To PS4)
Methodology (Taking Input)

## Slide 14
Pin Number | What it Indicates | Interpretation
Pin 1 | A Clock for Changing the State | Acts as a ‘Done’ or ‘Next’ Button in User interface
Pin 2 | Reset | Resets the Machine to IDLE State.
Pin 3,4,5 | Which Station | Motijheel= 3’b 000; Bangladesh Sec. = 3’b 001; Dhaka University= 3’b 010; Shahbagh= 3’b 011; Karwan Bazar= 3’b 100; (Any Other Value will give error)
Pin 6, 7,8 | Money input | 0 taka= 3’b 000; 5 taka = 3’b 001; 10 taka= 3’b 010; 20 taka= 3’b 011; 50 taka= 3’b 100; (Any Other Value will not change the total money)
Methodology (Taking Input)

## Slide 15
Pin Number | What it Indicates | Interpretation
PS1, PS2 | Rebate Code | Value of this two pulse acts as rebate code, in our design the correct rebate code is 2’b 11.
PS4 | Rebate Code Validation | Defines a state for taking the rebate code as input 0=rebate code can’t be inputted (rebate code is ignored) 1= rebate code can be inputted (rebate code is checked if it is right or wrong)
PS3 | Number of Passengers | Pulse 0 = 1 Passenger. Pulse 1 = 2 Passengers
Methodology (Taking Input)

## Slide 16
Showing Output
For the output part we will have,
Cost of the tickets
Total Amount of Input Money
Return Money
Ticket Buy Completed
Error
Methodology

## Slide 17
Input Money
(Last 2 Digit)
Total Cost
(Last 2 Digit)
Return Amount
Methodology (Showing Output)
Ticket Buy
Completed
Indicates if the Total Money in exceeds 100 or not
Indicates if the Total cost exceeds 100 or not

## Slide 18: State Diagram
IDLE
Next2
Next3
Next4
Error
Next1
Diff_st = 1/Fare = 7’d0
Diff_st = 2/Fare = 7’d0
Diff_st = 3/Fare = 7’d0
Diff_st =4/Fare = 7’d0
Anything else/Fare = 7’d0
Fare calculation FSM Block
Diff_st = abs(source_station – station)
Reset
If Reset=1 then the machine always comes to ‘IDLE’ State regardless of its current state

## Slide 19
Next2
Next1
Next1R
Next2R
Next3R
Next4R
Next3
Next4
Error
1,11/ 7’d25
0,xxx/ 7’d30
1,11/ 7’d35
0,xxx/ 7’d40
1,11/ 7’d45
0,xxx/ 7’d50
1,11/Fare = 7’d15
0,xxx/7’d20
Anything else/Fare = 7’d0
Fare calculation FSM Block
Input /Output Form
R.C.V=1, Rebate code=11/Fare = 7’d
2 bit Rebate Code
Rebate Code
Valid
State Diagram

## Slide 20: State Diagram
Next1R
Next2R
Next3R
Next4R
FinalFare
1/Fare = prev_fare<<1
1/Fare = prev_fare<<1
1/Fare = prev_fare<<1
0/Fare = prev_fare
0/Fare = prev_fare
0/Fare = prev_fare
0/Fare = prev_fare
1/Fare = prev_fare<<1
Fare calculation FSM Block
Input /Output Form
Passenger/Fare = 7’d

## Slide 21: State Diagram
FinalFare
ADD
clk/Sum = 0, Change = 0, Vend = 0
Total Money In Calculation FSM Block
Money_in && Sum<Fare /Sum = Sum + Money_in, Change = 0, Vend = 0

## Slide 22: State Diagram
ADD
Done
Sum>Fare/Sum =Sum, Change = Sum-Fare, Vend = 1
Total Money In Calculation FSM Block
clk/Sum = Sum, Change = Sum-Fare, Vend = 1
Money_in && Sum<Fare /Sum = Sum + Money_in, Change = 0, Vend = 0
IDLE
Reset=1
If Reset=1 then the machine always comes to ‘IDLE’ State regardless of its current state

## Slide 23: Sample Output
Source : Motijheel
Destination : Karwan Bazar (100)

## Slide 24: Sample Output
Rebate Code : 11 Fare= 45 Taka
Rebate Code Valid : 1

## Slide 25: Sample Output
Passenger : 1 Fare= 90 Taka

## Slide 26: Sample Output
Money In : 001 (5Tk)
Fare : 90 Tk
Money Input : 5 TK

## Slide 27: Sample Output
Money In : 100 (50Tk)
Fare : 90 Tk
Money Input : 105 Tk (100 Exceed LED on!)
Return : 15 Tk
Ticket Buy Completed LED ‘ON’

## Slide 28
Thank you